## Slide 1: lab: building water irrigation system that collects data using IOT
presented by :
Aboud Rayane

## Slide 2: Introduction
In this lab we are going to be building an irrigation system that will collect data from environment visualizate it in real time and send it to google sheet in order to use it in future projects.. All that using iot materials such as arduino wmos d1…

## Slide 4: Material used

## Slide 5: Controller:
The controller is the brain that will orchestrate the other parts of the system
It has three main functionality :
Collecting specific data from the environment
Controlling specific components of the system based on data collected
Sending this data to google sheets
[visualizing the data collection (this is an arduino cloud feature)]

## Slide 6: controller:
In our case our controller will be any type of arduino that can connect to internet using wifi (we can use wifi modules and plug it to arduino uno) in this lab we are going to be using Arduino wmos d1 which has esp8266
arduino wmos d1
arduino esp32
arduino uno + wifi module

## Slide 7: Data collection from environment

## Slide 8: Sensors:
Sensors are the intermediate part between our system and the environment, their main function is to translate a natural phenomenon into signal that our arduino can understand

## Slide 9: Sensors
Temperature and humidity sensor : in order to detect the temperature and humidity from the environment , in this lab we will be using DHT11
DHT11
DHT22

## Slide 10: Sensors
ultrasonic sensor : for this we will be using this component in order to detect the water level in the reservoir, (we could also use water level sensor)

## Slide 11: Sensors
soil moisture sensor : its role is to detect the degree of moisture in the ground

## Slide 12: Sensors
flow meter (optional): detects the amount of water that flows through it

## Slide 13: Component control

## Slide 14: Controllable components:
those are the components that will be controlled (activated or deactivated) by the controller (Arduino) based on conditions that are related to informations that are collected by the sensors

## Slide 15: Controllable components:
water pump : the role of this component is to get water from reservoir and release it in appropriate target

## Slide 16: Controllable components:
relay : a device that will be used to help the arduino control the motor (will be explained in details later..)

## Slide 17: Sending Data to google sheet

## Slide 18: Problem
Since using google sheet requires authentication and security stuff, our arduino cannot send data directly to the sheet file

## Slide 19: Solution
ifttt : a web service that will play the role of an intermediate computer (that google trusts) so that it will be allowed to write data on the file (it will be used in real time visualization)

## Slide 20: Visualization of data in real time

## Slide 21: Arduino iot cloud
Web and mobile application that will allow us to visualize all changes in our system (In a user friendly way)

## Slide 22: Assembly of the circuit components

## Slide 23: DHT11

## Slide 24: Ultrasonic sensor

## Slide 25: Soil moisture

## Slide 26: motor & relay

## Slide 27: Why do we need a relay ? couldn’t we just connect the motor directly to the arduino
Arduino cannot supply the motor with 5v of voltage
a motor would need 9v inorder to work
this is where the relay comes in
it will play the role of a barrage of a 9v power supply (battery)
the portal of the barrage is opened and closed by the arduino

## Slide 28: General schema of the project

## Slide 29: Creating a project in arduino cloud

## Slide 30: Creating a project in arduino cloud
Arduino cloud is the website that will allow us to visualize changes in our data in real time
You can think of a cloud as if it was a set of computers that will communicate with your arduino
it has a space to code our program
it has predefined libraries that are predefined (such as DH11 library)
it has a graphical user interface to simplify the work instead of programming everything manually

## Slide 31: Creating a project in arduino cloud
go to the official arduino website via this link and sign in
  https://www.arduino.cc/

## Slide 32: Creating a project in arduino cloud
go to the section : iot cloud

## Slide 33: Creating a project in arduino cloud

## Slide 34: Creating a project in arduino cloud

## Slide 35: Adding variables

## Slide 36: Adding variables
variables are the data which are in change and will affect on our system
In this project we will be using 4 main variables (to track visualize):
temperature
humidity
soil moisture
water level (for the simplification sake of the project we will actually display how far is the water from the sensor)

## Slide 37: Adding variables

## Slide 38: Adding variables

## Slide 39: Adding variables

## Slide 40: Adding variables
after adding variables :

## Slide 41: Associate the arduino with the project

## Slide 42: Associate the arduino with the project
Now it is time to let our arduino know the arduino cloud so that they can communicate with each other
we are going to be doing that by giving our arduino a name, and a secret key
a secret key is a security feature that allows a secure connection between the arduino board and arduino cloud

## Slide 43: Associate the arduino with the Arduino cloud

## Slide 44: Associate the arduino with the Arduino cloud

## Slide 45: Associate the arduino with the Arduino cloud

## Slide 46: Associate the arduino with the Arduino cloud

## Slide 47: Associate the arduino with the Arduino cloud

## Slide 48: Associate the arduino with the Arduino cloud

## Slide 49: Associate the arduino with the Arduino cloud

## Slide 50: Associate the arduino with the Arduino cloud

## Slide 51: Associate the arduino with the Arduino cloud

## Slide 52: Moving to the code …

## Slide 53: Moving to the code
The code is available on github (link provided later) the next section is for explanation purposes
the data is collected from environment using sensors and they are interpreted from arduino as specific values (analog [0-1023] or digital [0-1]) this is why you are going some lines of code when we transform the code from values that arduino understand to human readable values

## Slide 54: General structure of an Arduino program

## Slide 55: Data collection

## Slide 56: Temperature and Humidity sensor

## Slide 57: Ultrasonic sensor

## Slide 58: Soil moisture sensor

## Slide 59: Water pump sensor

## Slide 60: Sending data to google sheet

## Slide 61: connect the arduino to ifttt server

## Slide 62: connect the arduino to ifttt server
As we mentioned earlier we will be using ifttt server as intermediate between arduino and the google sheet, it will help us to visualize data in real time (from the cloud)
we are going to give the identity of our arduino to ifttt server and make them connect with each other so that ifttt server takes the data from your arduino board and write it in google sheet
the way it works is simple : if a change occurs in one of the variables arduino will send a signal to the ifttt and this one will be sending this to google sheet
there is a part in the final code where a function (send_data_to_sheet()) is executed this is the part where arduino will send it to ifttt and ifttt will handle the rest

## Slide 63: connect the arduino to ifttt server

## Slide 64: connect the arduino to ifttt server

## Slide 65: connect the arduino to ifttt server

## Slide 66: connect the arduino to ifttt server

## Slide 67: connect the arduino to ifttt server

## Slide 68: connect the arduino to ifttt server

## Slide 69: connect the arduino to ifttt server

## Slide 70: connect the arduino to ifttt server

## Slide 71: connect the arduino to ifttt server

## Slide 72: connect the arduino to ifttt server

## Slide 73: connect the arduino to ifttt server

## Slide 74: connect the arduino to ifttt server

## Slide 75: connect the arduino to ifttt server

## Slide 76: connect the arduino to ifttt server

## Slide 77: connect the arduino to ifttt server

## Slide 78: connect the arduino to ifttt server

## Slide 79: connect the arduino to ifttt server

## Slide 80: connect the arduino to ifttt server

## Slide 81: connect the arduino to ifttt server

## Slide 82: connect the arduino to ifttt server

## Slide 83: connect the arduino to ifttt server

## Slide 84: connect the arduino to ifttt server

## Slide 85: connect the arduino to ifttt server

## Slide 86: connect the arduino to ifttt server

## Slide 87: visualizing results in realtime

## Slide 88: visualizing results in realtime
This is the part where you can see the actual changes graphically on Arduino cloud
you can download the mobile version of Arduino cloud and log in from your account so that you can visualize those changes in from your phone

## Slide 89: visualizing results in realtime

## Slide 90: visualizing results in realtime

## Slide 91: visualizing results in realtime

## Slide 92: visualizing results in realtime

## Slide 93: visualizing results in realtime

## Slide 94: visualizing results in realtime

## Slide 95: visualizing results in realtime

## Slide 96: visualizing results in realtime

## Slide 97: visualizing results in realtime

## Slide 98: visualizing results in realtime

## Slide 99: Putting the code in the sketch

## Slide 100: Putting the code in the sketch
https://github.com/Rayane-Aboud/Irrigation_system/blob/main/code/code.ino
copy the code over there and paste it in the sketch section

## Slide 101: Putting the code in the sketch

## Slide 102: Putting the code in the sketch
Connect the arduino to your pc and run the program
if the arduino is not detected follow the instructions in this link :
https://support.arduino.cc/hc/en-us/articles/360014869820-Install-the-Arduino-Create-Agent

## Slide 103: References
Integrating IFTTT to arduino cloud:
  https://www.youtube.com/watch?v=YkA4TUgCmRA&t=1s
  https://www.youtube.com/watch?v=teY9xfSBxE4
DHT sensor tutorial :
  https://tutoduino.fr/debuter/capteur-temperature/
UltraSonic sensor tutorial :
  https://howtomechatronics.com/tutorials/arduino/ultrasonic-sensor-hc-sr04/
Soil moisture sensor:
  https://circuitdigest.com/microcontroller-projects/interfacing-soil-moisture-sensor-with-arduino-uno
Relay configuration:
  https://arduinogetstarted.com/tutorials/arduino-relay